## Slide 1
RHEM - 2018
Rangeland Hydrology
and
Erosion Model
Mark Nearing
Southwest Watershed Research Center
USDA-Agricultural Research Service
Tucson, AZ, USA
Presented by:

## Slide 2
Great Basin Rangelands
Research, USDA-ARS
Reno, Nevada
Northwest Watershed Research
Center, USDA-ARS
Boise, Idaho
RHEM Research Group
Mark Nearing
C. Jason Williams
Mariano Hernandez
Gerardo Armendariz
Mark Weltz
Sayjro (Kossi) Nouwakpo
Fred Pierson
Central National Technology
Support Center, USDA-NRCS
Dallas, Texas
Ken Spaeth
George Peacock (retired)
Southwest Watershed Research
Center, USDA-ARS
Tucson, Arizona
Olaf David
Texas A&M
Kingsville, Texas
Osama Al-Hamdan
Colorado State Univ.
Ft. Collins, CO

## Slide 3
Rangeland Hydrology and Erosion Model.
RHEM is a dynamic, event-based hillslope-scale infiltration , runoff and erosion model designed specifically for rangelands.
What is RHEM?

## Slide 4
“Rangelands are grasslands, shrublands, woodlands, wetlands, and deserts that are grazed by domestic livestock or wild animals.” (Wikipedia)
Rangelands are a sub-set of grazinglands, but generally refer to lands not suitable for agricultural crops.
They do not include pastures that are managed using agronomic practices, such as usually found in humid cropland areas.
What are rangelands?

## Slide 5: Rangelands
Great Basin, USA
Queensland, Australia
SW Arizona, USA
Kazakhstan

## Slide 6: Western US Rangelands

## Slide 7
What does RHEM do?
RHEM estimates runoff, erosion, and sediment delivery rates at the spatial scale of the hillslope.
RHEM is designed so to be used as a runoff and erosion calculator, or "engine", within a web-based interface and within other process-based models that apply to the watershed scale, such as AGWA/KINEROS2.
From the research perspective RHEM is a vehicle for incorporating new science from rangeland infiltration, runoff, and erosion research.

## Slide 8
RHEM Structure & Function
Fortran Core Engine
Parameter Estimation
User Interfaces
Applications

## Slide 9: 1. Core Engine
FORTRAN Executable is available for download from the RHEM web site.
Hernandez, Nearing, et al., 2017 WRR

## Slide 10
Hydrologic Processes
Kinematic Wave Dynamic Runoff Routing
Smith, R. E., D. C. Goodrich, D. A. Woolhiser, and C. L. Unkrich.(1995). “Chapter 20: KINEROS: A kinematic runoff
and erosion model”. In Computer Models of Watershed Hydrology. V. J. Singh, ed. Water Resources Publications.
Smith-Parlange Infiltration

## Slide 11
Dynamic Erosion & Sediment Routing
Bennett, J. P., 1974. Concepts of mathematical modeling of sediment yield. Water Resources Research, 10(3):485-492.
Bulygina, N.S. M. A. Nearing, et al., 2007. “DWEPP: A dynamic soil erosion model... ESPL, 32(7):998-1012.
Wei, H., M.A. Nearing, et al., 2009. A new splash and sheet erosion equation for rangelands. SSSAJ 73:1386-1392.
Nearing, M.A., et al., 1997. Hydraulics and erosion in eroding rills. Water Resources Research 33(4):865-876.
Foster, G.R. 1982. Modeling the erosion process. Chapter In: Hydrologic Modeling of Small Watersheds. ASAE Mono. 5.
Splash and Sheet sediment source term
Concentrated Flow sediment source term

## Slide 12: 2. Parameter Estimation
Translates information user-knowledge > model parameters.
The model is intended for land managers
Rangeland specialist understands:
Foliar and ground cover
Plant Lifeform
  Soil texture
  Slope steepness
Model Needs:
Erodibility
Effective Conductivity
Hydraulic Roughness
Etc…

## Slide 13: Experimental data
RHEM was first developed based on the WEPP-IRWET dataset 204 plots, 49 sites, 15 western states.
Database is expanded now with new data from Boise, Reno, Tucson

## Slide 14: Equations
Hernandez, Nearing, et al., 2017 WRR

## Slide 15: 3. User Interfaces
Web-based Interface
Stand-alone executable
KINEROS & AGWA watershed/geospatial models (USDA-ARS)

## Slide 16
RHEM web-based interface
The RHEM web tool is an online interface that allows users to input site information and review simulation results.
http://apps.tucson.ars.ag.gov/rhem/

## Slide 17
Uses information that rangeland specialists understand
Climate Station
Soil Texture Class
Slope
Steepness %
Shape Class
Foliar Cover
Bunch Grass %
Shrub/Tree %
Annual/Forbs %
Sod Grass %
Ground Cover
Litter %
Rocks %
Basal %
Bio-Crusts %
9 numbers & 3 dropdown choices

## Slide 18
RHEM web tool – Input Summary

## Slide 19
RHEM web tool – Output Summary
For a 300 year representative rainfall sequence

## Slide 20
Output – Scenario comparisons

## Slide 21
Stand-alone executable

## Slide 22
KINEROS and AGWA
RHEM is integrated with KINEROS for watershed management applications
AGWA is the geospatial interface for KINEROS

## Slide 23: 4. Applications How REHM is being used
Informing Ecological Site Descriptions (ESDs) S-T
Land Resource Inventory and Assessment (NRI)
Hillslope-scale engine within watershed models
USDA-NRCS Field Office
Research, teaching, and other applications with the web-based interface
Assessment of conservation practices (CEAP)

## Slide 24
Use 1 - Ecological Site Descriptions
An ecological site is “a distinctive kind of land with specific characteristics that differs from other kinds of land in its ability to produce a distinctive kind and amount of vegetation.”
Each ESD describes a state-and-transition model, which is a conceptual description of the long-term dynamics of an ecological site
ESDs are being developed and mapped over the entire US.

## Slide 25
Ecological Site Descriptions - ESDs
ESDs are being developed and mapped by NRCS, BLM, and FS across the entire US.
Methods have been developed to use RHEM to inform hydrologic function for ESDs
Williams, et al., 2016. Rangeland Ecology and Management 69:4-19.

## Slide 26
Example
Loamy Upland ESD:
305-406 mm (12-16 inches)

## Slide 27
Ecological States within the ESD
Historic Plant Community (HPC)
Shrub invaded state
Exotic perennial grass
Eroded
Loamy
Upland

## Slide 28
RHEM web tool – Input Information
Input information representing each state in the ESD

## Slide 29
RHEM web tool – Annual Runoff and Soil Erosion Output

## Slide 30
Risk Assessment
(a)
(b)
Yearly soil loss vulnerability relative to a user-defined baseline (e.g., HPC) - using probability.
User chooses a baseline scenario
Interface then gets yearly erosion values for a 300 year sequence
Determines the probability curves
Sets 4 Probability Groupings
Very High – Greatest 5% of years
To
Low - Least 50% of years
All other states in ESD compared to this baseline distribution of yearly soil loss rankings
KEY CONCEPT
pdf
cdf
Low
Med
High
Very High
for baseline

## Slide 31
RHEM web tool – Run Risk Assessment
HPC Historic Plant Community
chosen as the baseline
What the user sees and does

## Slide 32
Probability of Occurrence Matrix
HPC
Exotic
Grass
Shrub
Invaded
Eroded
1 out of 20 years
9 out of 10 years

## Slide 33
A useful tool for informing ESD development. Model is sensitive to differences in state conditions within the ESD State-and-transition model
The risk approach may have potential to serve as a method for defining Tolerable Soil Losses for Rangelands.

## Slide 34
Use 2- National Resource Inventory - NRI
Another Application
National Assessment of private lands, conducted since
the Soil and Water Resources Conservation Act of 1977.
Survey reported each 5 years
Statistical sampling with 800,000 points across the US

## Slide 35
RHEM and the NRI
Methods were developed to use RHEM to predict erosion for each NRI rangeland point
Hernandez et al., 2013
Methodology worked out on MLRA 41
2012 report
10,000 data points
w/ on-the-ground
site surveys

## Slide 36: Future Directions
USDA Handbook and user guide
Chapter in the ESD development handbook
Training Course in rangeland hydrology
Grid-based climate input
International climate data
Disturbance (fire)
Saline soils
Risk and Soil Loss Tolerance for rangeland

## Slide 37
http://apps.tucson.ars.ag.gov/rhem/
or go to the
USDA ARS Southwest Watershed Research Center
home page and follow the link to “Model Access”