## Slide 1
Updated Water and Wind Erodibility for Environmental Benefits Assessment in
Program Ranking
Olaf David, CSU
Rich Iovanna, FPAC
Dan Janes, FSA
Francesco Serafin, CSU
Shaun Case, CSU
Jack Carlson, CSU

## Slide 2
TERRA Application for Computing Erodibility/EBI

## Slide 3
TERRA Application for Computing Erodibility/EBI

## Slide 4
1950 1960 1970 1980 1990 2000 2010 2020 2040 2050
RWEQ
RUSLE2
WEQ (Cropland Wind)
RUSLE
USLE (Cropland Water)
Empirical Erosion Models (began when computing power was limited)
Process-Based Erosion Models (became possible with increasing computing power)
WEPP (Cropland Water)
WEPS (Cropland Wind)
RHEM (Rangelands Water)
Discontinued
?
Supported
Supported
Supported
Legacy to Current Erosion Technology

## Slide 5
  - Erodibility values more localized to CRP offer area
    Mapunit polygon vs. county extent mapunit
    10m DEM-based slope steepness vs. county extent mapunit steepness
    4K PRISM pixel adjusted climate input vs. county climate
  - More recent climate station data
  - WEQ technology no longer supported
  - WEPP and WEPS models cut from the same cloth
    Share common contemporary processes/methods
    Greater data commonality and compatibility
    Better integration with SWAT/APEX/EPIC water quality degradation vulnerabilities going forward
Major Reasons for Update

## Slide 6
Three WEPP/WEPS-Based Options for Erodibility Calculations
Response data flows for web services and data supporting three new options for water and wind erodibility

## Slide 7
Methods
Tilled fallow rotation object: 12 monthly rotary harrow operations, STIR 123
WEPP model service
  Calls wwesoilparams service to fetch soil mapunit/component list for area to be simulated
  Calls weppsoilinput service which fetches data from Soil Data Mart, processes and returns .sol input file
  Calls cligen_prism service which runs CLIGEN and returns PRISM adjusted .cli input file
  Calls operations service to fetch input parameters from CRLMOD for .man input file
  Calls average_slope service which returns average slope steepness for area to be simulated.
WEPS model service
  Calls wwesoilparams service to fetch soil mapunit/component list for area to be simulated
  Calls wepssoilinput service which fetches data from Soil Data Mart, processes and returns .ifc input file
  Calls cligen_prism service which runs CLIGEN and returns PRISM adjusted .cli input file
  Calls windgen service which runs WINDGEN and returns .win input file.
  Calls operations service to fetch input parameters from CRLMOD for .man input file
  Uses a 200x200 feet WEPS region

## Slide 8
Computing Load – CRP Erosion Database/Map (Option 3)
  17,334,000 CSIP crpassessment web service calls via publish/subscribe
  22 million WEPP and WEPS simulations (each)
  10 GB of json requests (17.3 M at 625 byte per request)
  82 GB of json responses (17.3 M at 5 KB per request)
  200 million internal service calls (soils, crlmod, slope, climate, ...)
  Total accumulated service execution time: 7.95 years
Supporting Infrastructure
  16 Kubernetes nodes with CephFS
  103 docker containers for wepp, weps, soils, climate, slope, crp, pub/sub
  400 cores, GB network; 4 webhooks
  Throughput 800,000 - 1 million CSIP runs per day

## Slide 9
Advantages/Disadvantages
(1) Full Model Simulation
Advantage: CRP offer area specific result; site-specific climate and slope steepness
Disadvantage: Takes 10-20 seconds to return result; more moving parts
(2) Surrogate Model
Advantage: CRP offer area specific result; site-specific climate and slope steepness; surrogate model takes less than 1 second to return result; fewer moving parts
Disadvantage: Takes ~5 seconds to fetch input data to surrogate model; surrogate model accuracy may not achieve NSE > 95% and RRMSE <10% in some areas.
(3) Database Lookup
Advantage: More site specific than legacy method; takes less than 1 second return result; fewest moving parts
Disadvantage: Not as site specific as options 1 and 2 (mupolygon-based); database requires update after annual July Soil Data Mart refresh

## Slide 10
CRP Tilled Fallow Erosion Map - Water
51 shape files, total size of 35 GB
17M polygons

## Slide 11
CRP Tilled Fallow Erosion Map - Wind

## Slide 12
CRP Tilled Fallow Erosion Map - Water

## Slide 13
CRP Tilled Fallow Erosion Map - Wind

## Slide 14
QA/QC – Iowa Example

## Slide 15
QA/QC – Iowa Example

## Slide 16
Erodibility = weighted average for 3 most prevalent mapunits in CRP offer area.

## Slide 17
Water and Wind Erodibility Comparisons

## Slide 18
Water and Wind Erodibility Comparisons

## Slide 19
Water Erodibility Comparison
Comparing 577 samples between 4 LRR

## Slide 20
Wind Erodibility Comparison

## Slide 21
Wind Erodibility: C and I factor analysis

## Slide 22
Discussion

## Slide 23
Water Erodibility Comparison - LRR M

## Slide 24
Wind Erodibility Comparison - LRR M

## Slide 25
Wind Erodibility C factor, I factor - LRR M

## Slide 26
Water Erodibility Comparison - LRR P

## Slide 27
Wind Erodibility Comparison - LRR P

## Slide 28
Wind Erodibility C factor, I factor - LRR P

## Slide 29
Water Erodibility Comparison - LRR B

## Slide 30
Wind Erodibility Comparison - LRR B

## Slide 31
Wind Erodibility C factor, I factor - LRR B

## Slide 32
Water Erodibility Comparison - LRR H

## Slide 33
Wind Erodibility Comparison - LRR H

## Slide 34
Wind Erodibility C factor, I factor - LRR H